## Slide 1: Sample scheme for supmod_dummy
supmod_dummy.py
fancy process 1
…
…
awesome process 2
…
…
wonderful database
trajectory
map
score

## Slide 2: Scheme for supmod_ static_ environment
supmod_static_environment.py
friction / acceleration check
determine requested lat. & long. acceleration
check for friction circle compliance
trajectory
map
score
map-check
ray-tracing based on
occupancy-grid
patch intersection based on lanelets (bound-arrays)
depending on map-format
valid
valid
kinematic / dynamic check
check if turn radius is not violated
valid
safe end-state check
check if end-state of traj. is safe (here: v=0m/s)
valid

## Slide 3: Scheme for supmod_ static_collsion
supmod_static_collision.py
trajectory
map
score
map-check
ray-tracing based on
occupancy-grid
patch intersection based on lanelets (bound-arrays)
depending on map-format

## Slide 4: Scheme for supmod_ friction
supmod_friction.py
friction / acceleration check
determine requested lat. & long. acceleration
check for friction circle compliance
trajectory
score

## Slide 5: Scheme for supmod_ safe_end_sate
supmod_safe_end_sate.py
trajectory
score
safe end-state check
check if end-state of traj. is safe (here: v=0m/s)

## Slide 6: Scheme for supmod_ kinematic_dynamic
supmod_kinematic_dynamic.py
trajectory
score
kinematic check
check if turn radius is not violated
dynamic check
check if motor acc. limits are respected

## Slide 7: Scheme for supmod_ rules
supmod_rules.py
rule n
check if rule n holds
trajectory
score
rule 1
check if rule 1 holds
rule 2
check if rule 2 holds
…

## Slide 8: Scheme for supmod_rule_reach_sets
supmod_rule_reach_sets.py
calculate occ. sets
calculate future ego occupation
calculate reachable set for all object vehicles
evaluate rules
evaluate which rules are active
calculate reduction patches for active rules
reduction patches
score
reachable sets
evaluate intersections
evaluate for set intersections (equal )
ego occ. patches
obj.-list
trajectory
map
\
\
Caution: means in this illustration that the set difference between the lower and upper input is drawn.

## Slide 9: Scheme for supmod_guaranteed_occupancy_area
supmod_guaranteed_occupancy_area.py
determine occ. sets
calculate future ego occupation
extract guaranteed set for all object vehicles
init (only called once)
initialize guaranteed occupation database on first call
score
ego occ. patches
evaluate intersections
evaluate for set intersections (equal )
guaranteed occupation
obj.-list
trajectory
guaranteed occupation database

## Slide 10: Scheme for supmod_ integrity
supmod_integrity.py
trajectory
score
basic checks
check for proper dimensions
check for valid physical range
valid
valid
check curvature
compare curvature in traj. to change of heading over time
valid
check acceleration
compare change of velocity to provided acceleration
valid
check heading
relate heading determined via xy-coords to provided one
check s-coordinate
compare s-coordinate of trajectory to xy-distances
valid